SERVICE SCHEDULE x191 - TELSTRA WHOLESALE SPECTRUM SHARING SERVICE

Service Schedule x191 –Telstra Wholesale Spectrum Sharing Service 	2

1	Definitions	2

2	Service Description	3

3	Splitters and Network Termination Devices	5

4	Access Seeker Obligations	5

5	Facilities Access	6

6	End Customer Billing	6

7	Other Provisions	6

Record of Issues

Service Schedule x191 –Telstra Wholesale Spectrum Sharing Service

# Definitions

ADSL means an Asymmetric Digital Subscriber Line service operated in accordance with the performance requirements of the Network Deployment Rules.

Authorised Equipment means:

### equipment that complies with the Network Deployment Rules excluding Deployment Class 6c; and

### equipment that complies with the Telstra Splitter Specification.

Deployment Class has the meaning set out in the Network Deployment Rules.

Deployment State B has the meaning set out in the Network Deployment Rules.

IRIM means an integrated RIM.

MDF means main distribution frame.

Network Deployment Rules means the Industry Code entitled Unconditioned Local Loop Service - Network Deployment Rules registered by the ACA under section 117 of the Telecommunications Act.

RIM means remote integrated multiplexer which is a pair gain system that employs multiplexing to derive circuits and which provides dial tone, ring current and battery feed.

RSS means a remote subscriber stage which provides dial tone, ring current and battery feed.

RSU means a remote subscriber unit which performs an equivalent function to an RSS.

Splitter means the equipment that separates the voice and non-voice ADSL spectrum and complies with the Telstra Splitter Specification.

Telstra Customer Access Module (TCAM) is a device owned by Telstra that provides dial tone, ring current and battery feed to customer equipment.  Examples include an RSS, RIMs an RSU and an IRIM.

Telstra Splitter Specifications means the Telstra Splitter Specification for ADSL/POTS Spectrum Sharing Technical Reference RCIT.0004 as provided at http://www.telstra.com.au/adsl/equipment.htm from time to time.

Telstra Wholesale Spectrum Sharing Service means the service provided by Telstra under this Service Schedule and described in paragraph 2.2.

SSS Boundary means in relation to a line that enters a building on the SSS End Customer premises:

(a)	if there is an MDF in the building and the line is connected to the MDF - a two wire point on the side of the frame nearest to the Telstra network; or

(b)	if paragraph (a) does not apply but the line is connected to a network termination device located in, on or within close proximity to, the building - the side of the device nearest to the SSS End Customer; or

- if neither paragraph (a) nor (b) applies - the network boundary point ascertained in accordance with section 22 of the Telecommunications Act.

SSS End Customer means an end customer or proposed end customer to whom the Access Seeker supplies or proposes to supply a telecommunication service using a Telstra Wholesale Spectrum Sharing Service.

SSS End Customer Premises means premises of a SSS End Customer to which the Telstra Wholesale Spectrum Sharing Service is or will be provided.

SSS Interconnection Cable means a cable connecting one or more twisted metallic pairs between a MDF at a Telstra local exchange or a RIM, as the case requires, and the SSS POI.

SSS POI means, in relation to a line, a point that is an agreed point of interconnection located at or with a TCAM and located on the SSS End Customer side of the TCAM.

# Service Description

Telstra Wholesale Spectrum Sharing Service

## The following service description is provided for the Telstra Wholesale Spectrum Sharing Service and applies to the provision of the Telstra Wholesale Spectrum Sharing Service by Telstra to the Access Seeker.

## The Telstra Wholesale Spectrum Sharing Service is a service for the provision of access to the non-voice ADSL frequency spectrum (in accordance with the Telstra Splitter Specification) of a continuous metallic twisted pair between the SSS Boundary at the SSS End Customer Premises and a SSS POI associated with the TCAM serving that SSS End Customer that Telstra is currently using to provide an active PSTS voice service.

## The Telstra Wholesale Spectrum Sharing Service is illustrated in the following diagram and contains the options set out below:

### Option 1 - SSS Boundary (a):  the Access Seeker installs jumpering to the MDF and installs the Splitter (either a centralised splitter or an in-line filter), at the Access Seeker’s option.

### Option 2 -SSS Boundary (b):  the Access Seeker installs the Splitter (a centralised splitter) and a network termination device at the SSS End Customer Premises.

### Option 3 -SSS Boundary (c):  the Access Seeker installs the Splitter (an in-line filter) at the SSS End Customer Premises.

## To avoid doubt, the Telstra Wholesale Spectrum Sharing Service does not include:

### access to spectrum where ISDN is being used to provide the active PSTS voice service on the line;

### access to spectrum where the TCAM is not located in a Telstra exchange, until such time as suitable interconnection arrangements are agreed between Telstra and the Access Seeker or there has been a transition to Deployment State B in accordance with the Network Deployment Rules; or

### any links between a Telstra exchange and a RIM (when RIM fed arrangements are agreed under (c)).

Availability

## The availability of the Telstra Wholesale Spectrum Sharing Service may vary depending on geographic and technical capability of the Telstra network at the time at which a request for the Telstra Wholesale Spectrum Sharing Service is made or the Telstra Wholesale Spectrum Sharing Service is delivered.

Industry Standards and Over Voltage Protection

## The Telstra Wholesale Spectrum Sharing Service does not include the provision of over voltage protection to safeguard against personal injury and damage to the Access Seeker’s equipment or equipment belonging to third parties.  The Access Seeker acknowledges that Telstra does not install over voltage protection, as a matter of standard practice, in SSS End Customer Premises.

## The Access Seeker must, at its own cost, install Telstra approved over voltage protection on the “equipment side” of Telstra’s MDF prior to acquiring the Service.  The “equipment side” and the point of over voltage installation are illustrated in the diagram in paragraph 2.3.

## The Access Seeker may also, at its own cost, install over voltage protection on the Access Seeker’s side of the SSS POI and at the SSS End Customer Premises.

## Where the Access Seeker installs over voltage protection under paragraphs 2.7 or 2.8, it must comply with all applicable industry safety standards, including the specifications set out in the Network Deployment Rules for voltages and currents.

# Splitters and Network Termination Devices

Splitter Specification

## The Access Seeker is responsible for providing the Splitter at both the SSS End Customer Premises and at the SSS POI.  The Splitter must comply with the Telstra Splitter Specifications.

# Access Seeker Obligations

## The Access Seeker must use best endeavours to ensure that the integrity of the underlying Telstra PSTS service is not compromised by it or the SSS End Customer.

## The Access Seeker must comply with Deployment Class 6 (excluding 6c) of the Network Deployment Rules.

## The Access Seeker must cooperate with Telstra as reasonably required to ensure that end-user privacy rights are not infringed and may not record or monitor communications carried on the underlying PSTS service.

## The Access Seeker may only use the Telstra Wholesale Spectrum Sharing Service to operate an ADSL service in accordance with Deployment Class 6 (excluding 6c) of the Network Deployment Rules.

# Facilities Access

## The Access Seeker will need to enter into with Telstra such facilities access arrangements as are necessary in order for it to connect its network to a Telstra Wholesale Spectrum Sharing Service at the SSS POI.  However facilities access is not a matter dealt with by this Undertaking.

# End Customer Billing

## The Access Seeker is responsible for billing the SSS End Customer for the telecommunications service provided by the Access Seeker to the SSS End Customer.

# Other Provisions

Network Modernisation

## The Access Seeker agrees that the provision of the Telstra Wholesale Spectrum Sharing Service does not prevent, limit or restrict Telstra from modernising its Network.

## The Access Seeker acknowledges that:

### Network modernisation by Telstra may include the installation of RIMs closer to SSS End Customers than traditional exchange buildings;

### Network modernisation may require the truncation of the Telstra Wholesale Spectrum Sharing Services provided from traditional exchange buildings, the relocation by Access Seekers of SSS POIs from exchange buildings to the vicinity of relevant RIMs and/or the alteration of Deployment Classes of Authorised Equipment used by Access Seekers on the Telstra Wholesale Spectrum Sharing Service; and

### where Network modernisation does not result in the truncation of the Telstra Wholesale Spectrum Sharing Service provided to the Access Seeker, but requires the alteration of the Deployment Class of Authorised Equipment used on the Telstra Wholesale Spectrum Sharing Service, then subject to the required alteration to the Deployment Class, the Access Seeker may continue to access the Telstra Wholesale Spectrum Sharing Service.